HercuLine 2000 series

简介 HercuLine 2000 系列执行机构, 控制: 上/下CAT, PAT, DAT有数字/可编程电子和继电器输出, 非接触式位置传感, 无背驱无制动设计, 输入/输出 (4 mA 到 20 mA, 1.0 V 到 5.0 V, 数字)。 产品描述 Herculine™ 执行器为所要求的环境提供高可靠性和低维护量。稳定的结构和连续负载马达减少了总体维护成本并消除了意外的事故。这些特性与艺术级的电子单元相结合确保执行器运行寿命中精确和可重复的性能。 Herculink™ PDA 软件能访问作为Herculine™ 2001, 2002, 10260S and 11280S执行器标准的程序和通讯功能，而无需增加就地键盘和显示HMI的费用。使用一个Palm™ PDA 和 Herculink™ 软件和一个RS232/485 转换器您能就地或对执行器远程配置，标定和访问信息。 特征 Herculine 2000 开/关控制 位置比例控制 自锁/解锁齿轮传动链 90 ° 和150 °可调行程 对于150°行程的16.0秒到75.0秒行程时间 Herculine 2001 - Herculine 2000的所有主要特性外加： 数字，可编程电子单元 电流或电压远程设置点控制 可选的就地显示和键盘 Modbus RTU通讯 Herculink™ Palm™ PDA软件兼容 可选的可编程继电器输出 Herculine 2002 - Herculine 2001的所有主要特性外加： Non-contact position sensing 非接触式位置传感 Programmable relays 可编程继电器 Auto/Manual switch 自动/手工切换 典型应用 Dampers 挡板 蝶形阀门 旋转轴阀门

HercuLine 2000 series Action required Rotary Programmable/Communications Yes Torque/thrust 6 N-m to 45 N-m [4 lb-ft to 33 lb-ft] Position Sensing Non-contact or Potentiometer Repeatability 0.20 Duty cycle Continuous Ambient operating temperature -30 °C to 75 °C or 85 °C [-20 °F to 170 °F or 185 °F] Input Signal Type 4 mA to 20 mA, 1 V to 5 V, Digital, PAT Position Output None, 4 mA to 20 mA, 1 V to 5 V, 135 ohm or 1,000 ohm, Slidewire Emulation End of Travel Limit switches Two standard Auxiliary Outputs 4 switches or 4 relays Approval CE, CSA, UL Availability Global